STAIR NOSING SPECIFICATIONS

PART 1 — GENERAL

1.01 RELATED DOCUMENTS

A. Drawings and general provisions of the Contract, including General Conditions, Supplementary Conditions and Division-1 General Requirements, apply to the work of this section.

1.02 WORK INCLUDED

A. Furnish and install complete Balco, Inc. Stair Nosings.

1. Saf-T-Glo finish for ribbed safety treads.

2. Two-Component stair nosing systems.

3. Solid Bronze stair nosing systems.

4. Single Component stair nosing systems.

5. Non-slip abrasive strips and bars.

6. Stair nosing systems for special applications.

7. Stair nosing systems for renovations.

8. Cast [Aluminum] [Iron] stair nosing systems.

1.03 RELATED WORK

A. Related work which is specified elsewhere.

1. Concrete work: Section 03000.

2. Unit Masonry: Section 04200.

1.04 REFERENCES

A. Publications listed herein are part of this specification to the extent referenced. The criteria established in the specifications shall take precedence over the standards referenced herein. (Examples of reference standards are given below.)

1. American Society for Testing and Materials (ASTM):

- ASTM B 221 Standard Specification for Aluminum and Aluminum-Alloy Extruded Bars, Rods, Wire, Shapes and Tubes

- State of California Title 24, Stripping code for the visually impaired

1.05 SYSTEM DESCRIPTION

A. Stair nosing assemblies shall be [anchored to substrate] [cast-in-place].

B. Stair nosing treads shall be [solid] [ribbed].

C. Stair nosing tread surfaces shall be slip resistant.

D. Stair nosing treads shall be removable and replaceable.

E. Retrofit stair nosings shall be [bevel back] [square back].

F. Stair nosing treads shall meet OSHA Barrier-Free Code requirements for stair design in public buildings.

G. Stair abrasive bars shall be [1 inch] [2 inch] wide anti-slip bars.

H. Abrasives with cementious-based resins shall not be acceptable.

1.06 QUALITY ASSURANCE

A. Manufacturer: Obtain stair nosing assemblies through one source from a single manufacturer.

1. Manufacturer shall be ISO 9001:2000 Certified.

a. The Manufacturer shall have documented management and control of the processes that influence the quality of its products.

b. The Manufacturer shall have documented management and control of the processes that influence the quality of its customer service.

2. Manufacturer shall have a minimum of ten (10) years of experience in the fabrication of stair nosing systems.

B. Installer: Firm with not less than three (3) years of successful experience in the installation of systems similar to those required by this project and acceptable to the manufacturer of the system.

1.07 SUBMITTALS

A. Submit manufacturer’s specifications and technical data, including Material Safety Data Sheets, installation instructions, as required, and catalog cuts and templates where required to explain construction and to provide for incorporation into the project.

B. Submit certificates and/or copies of independent test reports or research reports showing compliance with specified performance requirements.

C. Submit shop drawings showing complete fabrication details for all stair nosings, including required anchorage to surrounding construction.

D. Submit three (3) 6" samples of the specified system.

1.08 DELIVERY, STORAGE AND HANDLING

- The manufacturer shall fill stair nosing sub-channels with a protective material to provide protection during construction.

- Prior to shipment, the manufacturer shall cover the abrasive with heavy-duty tape to eliminate concrete infiltration and staining.

- Deliver [stair nosing assemblies] [abrasive bars] to jobsite in new, clean, unopened crates of sufficient size and strength to protect materials during transit.

- Store components in original containers in a clean, dry location.

1.09 WARRANTY

A. Submit manufacturer’s warranty that materials furnished will perform as specified for a period of not less than one (1) year when installed in accordance with manufacturer’s recommendations.

PART 2 — PRODUCTS

2.01 ACCEPTABLE MANUFACTURERS

A. Furnish and install as noted in specifications and as indicated on drawings, [stair nosing (model and type no.)] [Abrasive bars (type no.)] as manufactured by: Balco, Inc., P.O. Box 17249, 2626 S. Sheridan, Wichita, KS 67217; phone: 800-767-0082 or (316) 945-9328; fax: (316) 945-0789.

2.02 MATERIALS

A. Stair nosing system: [Manufacturer’s model and type number].

1. Aluminum: ASTM B 221, alloy 6063-T5 for extrusions.

2. Bronze: Alloy 385 for extrusions.

3. Cast Aluminum: Class 30 Aluminum, tread plate.

4. Cast Iron: Class 35, tread plate.

B. Abrasive: Two (2) part Epoxy combined with aluminum oxide grit.

C. Fasteners required for complete installation to manufacturer’s instructions.

- Two Component Stair Nosings: Standard and Tread plate securing screws.

- Single Component Stair Nosings: [Standard] [Barbed] [Continuous] [Strap] anchors.

- Special Applications Stair Nosings: [Standard] [Concrete Screws].

- Stair Nosings for Renovations: [Wood Screws] [Strap Anchors] [Concrete Screws]

- Cast Stair Nosings: Wing Anchor.

2.03 FABRICATION

A. Fabricate stair nosing assemblies as detailed.  Provide anchors and accessories necessary for complete installation.

- Fabricate solid surface abrasive tread 3/8 inch thick by [__________] wide.

- Fabricate heavy-duty abrasive tread ribs ¼ inch thick by [__________] wide.

- Fabricate stair nosings with the depth of nose to measure underside [__________] inches.

- Provide [abrasive treads] [abrasive bars] of the specified color.

- Provide [Saf-T-Glo finish on abrasive treads.

- Provide specified anchors and, where required, tread plate securing screws.

- Surfaces to be embedded in concrete shall be coated with a clear acrylic lacquer.

B. Package components with anchors.

2.04 FINISHES

A. Aluminum subchannels and tread plates shall be:

- Mill finish.

- Heat-treated for strength.

- Clear acrylic lacquer coated for components to be embedded in concrete.

B. Bronze tread plates shall be:

1. Satin finish.

C. [Solid abrasive tread] [abrasive ribs] shall be: [BR-1 Earth Brown] [C-15R Silver Gray] [C-35R Terra Cotta] [SG-L80 Saf-T-GloTM Yellow] [C-10 Black (standard)] [R-1 Redwood] [GR-2 Cactus Green] [SG-C15R Saf-T-GloTM Silver Gray] [Other].

- Cast Iron shall be prime painted.

PART 3 — EXECUTION

3.01 EXAMINATION

A. Installer shall examine conditions under which work is to be performed and shall notify the contractor in writing of unsatisfactory conditions. Installer shall not proceed until unsatisfactory conditions have been corrected in a manner acceptable to the installer.

3.02 INSTALLATION

A. Install stair nosings in accordance with the governing regulations, the industry standards applicable to the work, and the manufacturer’s written installation instructions.

- Sub-channels of two component stair nosings shall be installed with the pour.

- Abrasive tread plates of two component stair nosings shall be installed in the final stages of construction.

B. Work shall be aligned plumb, level, and, where required, flush with adjacent surfaces and rigidly anchored to the substrate.

3.03 CLEANING

A. Clean exposed surfaces as recommended by the manufacturer.

3.04 PROTECTION

A. Advise the contractor of procedures required to protect the finished work from damage by work of other Sections during the remainder of the construction period.

B. Finished units shall be without damage. Units damaged during shipping or construction shall be repaired by the contractor at the expense of the party damaging the material, in accordance with the contract requirements.

3.05 GENERAL RESPONSIBILITY

A. Any variation from this specification resulting in additional cost to any other contractor or subcontractor on this project shall be the sole financial responsibility of the contractor for the work of this section.